## Slide 1
COMMUNICATION DESIGN PROJECT
Team Starlink
BASNAYAKE B.M.N.S. 220072R
PELAGEWATTA H.P. 220455U
PATHIRANA P.N.A . 220449F

## Slide 2
PROJECT OVERVIEW
  Objective: Develop a point-to-point communication system that can transmit images, voice, and video wirelessly in the 2.4 GHz ISM band.
  Key features:
  Digital modulation techniques
  GNU Radio for signal processing
  BladeRF for hardware implementation

## Slide 3
DESIGN METHODOLOGY
REQUIREMENT ANALYSIS
Point-to-point digital wireless communication system in 2.4 GHz ISM band.
Should be able to transmit images, voice and video
SELECTION OF MODULATION SCHEME
Selecting QPSK for higher data rate and bandwidth efficiency
IMPLEMENTATION IN GNU RADIO.
Identifying blocks and their arrangement.
Designing the flowgraph.
Simulate transmission with virtual channel model.
1
2
3

## Slide 4
WHY QPSK?
  High Bandwidth Efficiency: Transmits 2 bits per symbol.
  Spectral Efficiency.
  Doubled data rate over BPSK.
  Balanced tradeoff between complexity and performance than BPSK
  Similar power efficiency in practice to BPSK

## Slide 5
BPSK
  Simplicity: Easy to implement and debug.
  Less bandwidth efficient than QPSK.
  Robustness: Performs well in noisy environments with low bit error rates.
  Power Efficiency: Operates effectively at low power.
  Simple Receiver: Straightforward design for modulation and demodulation.

## Slide 6
BASIC IDEA OF THE FLOWGRAPH

## Slide 7
DESIGN METHODOLOGY
HARDWARE SETUP USING BLADERF
Transmitting through a real channel with the use of BladeRf
IMPLEMENTING
POINT TO POINT TRANSMISSION
Using 2 devices to implement the point to point communication system
4
5
TESTING AND PERFORMANCE OPTIMIZATION
Updating the flowgraph based on the errors encountered when transmitting point to point through a real channel
6

## Slide 8
WIRELESS COMMUNICATION USING BLADERF
We utilize the BladeRF device for wireless communication, opting for practical implementation over simulation by using the SoapyBladeRF Source and SoapyBladeRF Sink blocks into the flowgraph to directly interface with the BladeRF hardware.
SoapyBladeRf Source Block
is used to receive signals from the BladeRF device. This block captures incoming signals from the air and allows processing them for further operations.
SoapyBladeRf Sink Block
is used to transmit processed data via the BladeRF device. This block sends the modulated signal to the BladeRF for transmission.

## Slide 9
CHALLENGES ENCOUNTERED
SYNCHRONIZATION ISSUES
Timing mismatches caused decoding errors (when transmitting images). Resolved this by adding a preamble.
CHANNEL INTERFERENCE
Interference from Wi-Fi and Bluetooth degraded signal quality.
ERROR HANDLING
Noise in the channel introduced data errors. We addressed this with robust error detection and correction codes.

## Slide 10
TRANSMITTER FLOWGRAPH

## Slide 11
RECEIVER FLOWGRAPH

## Slide 12
FILE SOURCE
We used the File Source block to get the bit stream input.We take any input as a tmp file. This is done by a custom python code in the directory.
Key Features:
  Converts the input source into characters and then a header and a tail is added to identify the beginning and the end .
  A preamble and a filler is also added for synchronizing purposes .
  This method is used to protect the meta data(File formats etc).
STREAM TO TAGGED STREAM
The Stream to tag Stream block converts a continuous stream of data into packets of 8 bytes by adding tags. This define the start and end of a packet.
This packetizing step for the following framing process.

## Slide 13
FORWARD ERROR CORRECTION
The FEC Extended Tagged Encoder and Decoder blocks in GNU Radio implement Forward Error Correction (FEC) using tagged streams.
FEC Extended Tagged Encoder
Adds redundancy to the input data based on convolutional codes. This redundancy helps detect and correct errors during transmission.
FEC Extended Tagged Decoder
Uses the redundant information to identify and correct errors in the received data, improving reliability.
Parameters: Constraint length-7 , Rate-1/2

## Slide 14
FRAMING
The Protocol Formatter block generates a header using a specified format and appends it to the tagged stream. Here we use a 32 bit (4 byte) access code.
The Tagged Stream Mux block combines the payload stream and the generated header stream into a single stream.

## Slide 15
CONSTELLATION MODULATOR
CONSTELLATION
Defines the modulation type using a modulation object. Here we use QPSK. So, we map the bits to 4 symbols with 2 bits per symbol.
DIFFERENTIAL ENCODING
Here we set differential encoding to ‘Yes’
SAMPLES/SYMBOL
This upsamples the symbols with a factor of 4
The constellation modulator block modulates a stream of bits into complex baseband symbols. It has the following parameters.
EXCESS BANDWIDTH
Uses a root-raised cosine (RRC) filter with a roll-off of 0.5Hz for pulse shaping. This helps to minimize inter-symbol interference (ISI).

## Slide 16
USING SYMBOL SYNC BLOCK
The Symbol Sync block is used for accurate clock recovery and synchronization of symbols in the received signal. It adjusts for timing offsets and ensures symbols are correctly sampled at their optimal points.
Why Used Instead of Polyphase Clock:
  Flexibility: Symbol Sync supports various synchronization algorithms, offering better adaptability to different modulation schemes like BPSK.
  Ease of Configuration: Provides a simplified interface for fine-tuning parameters compared to the more complex polyphase clock approach.
  Improved Performance: Offers higher accuracy and stability in symbol timing recovery, essential for reliable data decoding in your project.

## Slide 17
The Differential Decoder block decodes data that was encoded using differential encoding. It recovers the original bit sequence by comparing the phase or state changes between consecutive symbols.
The Constellation Decoder block Maps received complex symbols back to their corresponding bit sequences according to QPSK modulation we defined earlier.
The Linear Equalizer block compensates for channel distortions like multipath fading or inter-symbol interference (ISI). Here it uses a CMA algorithm (Constant Modulus Algorithm). This corrects the error of diffrent amplitudes in the constellation diagram.
The Costas Loop block is used for carrier frequency and phase synchronization. It tracks and corrects phase offsets in the received signal.
1
4
2
3

## Slide 18
STREAMING
Transmitter Side-
  The VLC media player is given access to the camera and the input video stream is saved as in.ts file and constantly updated
  The file is repeatedly read and sent through the transmitter.
Reciever Side-
  The received data is read and it is displayed through the receiver side VLC

## Slide 19
GUI
The user interface is developed using python and customtkinter library.
You can Send, Recieve or Stream

## Slide 20
Sending And Receiving GUI’s

## Slide 21
PERFORMANCE FIGURES
  Data Rate between 196-226 kbps
  Maximum distance that can be transmitted: 40-45 ft
We tested the point-to-point communication system at various distances and ensured reliable and accurate data transmission up to around a distance of 45 feet
We transmitted a file of known size and measured the time taken for its transfer to determine the data rate of the communication system.

## Slide 22
THANK YOU